## Slide 1: Lab 4 - Arithmetic
EcEn 220

## Slide 2: Common Errors
Signal order is wrong
Output = Input
co[7]

## Slide 3
wrong module name: Arithmetic_Top or
wrong signal name: Sw that do not match testbench
Input and output swapped
missing “wire”, wrong width [0:15] or sw[15:0]
add redundant output co: mismatch w/ testbench
declare the same signal twice
logic overflow;
wrong width [15:8] or b[7:0]
wrong B sign bit – should not be sw[15]
wrong B sign bit – should not be sw[15]
wrong b – should not be sw[15:8]

## Slide 4: Lab 4
2's complement binary addition, subtraction, and overflow detection
2's complement binary adder
Hierarchical design
Testbench to validate the design

## Slide 5
2’s Complement Binary to Decimal
10000100 -124
00011001 25
Negate 2’s Complement Binary
01111100 124
11100111 -25
2’s Complement Binary Addition
10000100 (-124) + 01100100 (100) = 11101000 = -24
01111111 (127) + 10011001 (-103) = 00011000 = 24
01111111 (127) + 01100111 (103) = 11100110 Overflow
00011010 (26) + 01001001 (73) = 01100011 = 99
11100110 (-26) + 10110111 (-73) = 10011101 = -99
10000100 (-124) + 10011001 (-103) = 00011101 Overflow
2’s Complement Binary Subtraction
10000100 (-124) - 01100100 (100) = 00100000 Overflow
01111111 (127) - 10011001 (-103) = 11100110 Overflow
01111111 (127) - 01100111 (103) = 00011000 = 24
00011010 (26) - 01001001 (73) = 11010001 = -47
11100110 (-26) - 10110111 (-73) = 00101111 = 47
10000100 (-124) - 10011001 (-103) = 11101011 = -21
sw = 0110010010000100
sw = 1001100101111111
sw = 0110011101111111
sw = 0100100100011010
sw = 1011011111100110
sw = 1001100110000100
sw = 0110010010000100
sw = 1001100101111111
sw = 0110011101111111
sw = 0100100100011010
sw = 1011011111100110
sw = 1001100110000100

## Slide 6: 2’s Complement Binary to Decimal
  00011001 ->
  10000100 ->

## Slide 7: Sign Extension from 8 bits to 9 bits
  10000100 ->
  00011001 ->
110000100
000011001

## Slide 8: Negate 2’s Complement Binary
01100111 ->
10011000 + 1 =
10100100 ->
01011011 + 1 =
+103
-103
-92
10011001
01011100
+92

## Slide 9: Addition of Two 2’s Complement Numbers
10000100
+ 00111111
11000011
-124
63
-61
01100111
+ 10100100
00001011
+103
- 92
+ 11

## Slide 10: Subtraction of Two 2’s Complement Numbers
10000100
- 10011001
-124
-103
- 21
01100111
- 11101011
+103
- 21
+124
10000100
+ 01100111
11101011
-124
+103
-21
01100111
+ 00010101
01111100
+103
+ 21
+124

## Slide 11: Full Adder Derivation
A | B | Cin | Cout | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1
Cout = A’BCin+ AB’Cin + A BCin’+ ABCin
= A’BCin+ ABCin
+ AB’Cin + ABCin
+ A BCin’+ ABCin
= BCin + ACin + AB
S = A’B’Cin + A’BCin’+ AB’Cin’ + ABC
= A  B  C

## Slide 12: Single-bit Full Adder
Si
Ci+1
Ai
Bi
Ci
Ai
Bi
Bi
Ci
Ai
Ci
Si
Ci+1
Ci
Full
Adder
Ai
Bi

## Slide 13: Single-Bit Full Adder
Use structural SV to build a single-bit full adder.
Create a tcl file to perform simulation on your design for all 8 possible input conditions.
A | B | Cin | Cout | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1
module FullAdd(
input wire logic a,
input wire logic b,
input wire logic cin,
output logic s,
output logic co
);
…….
endmodule

## Slide 14: 8-Bit Adder
module Add8(
input wire logic [7:0] a,
input wire logic [7:0] b,
input wire logic cin,
output logic [7:0] s,
output logic co
);
…….
endmodule
Full Adder
Full Adder
Full Adder
A0 B0
A1 B1
A2 B2
S0
S1
S2
cin
C2
C1
Full Adder
A3 B3
S3
C3
Full Adder
Full Adder
Full Adder
A4 B4
A5 B5
A6 B6
S4
S5
S6
C6
C5
Full Adder
A7 B7
S7
C7
C4
co
Use SV hierarchy to combine eight single-bit adders to one 8-bit adder.

## Slide 15: 8-Bit Adder
Refer to Chapter 11 how to use SV hierarchy.
Simulate your design with a new tcl file that assign all 8 bits with single add-force command.
For example, add_force cin 0
add_force a 10001010
add_force b 00001010
run 10 ns
Full Adder
Full Adder
Full Adder
A0 B0
A1 B1
A2 B2
S0
S1
S2
cin
C2
C1
Full Adder
A3 B3
S3
C3
Full Adder
Full Adder
Full Adder
A4 B4
A5 B5
A6 B6
S4
S5
S6
C6
C5
Full Adder
A7 B7
S7
C7
C4
co

## Slide 16
1. Adding a positive binary number to a negative binary number.
2. Adding two positive binary numbers without overflow.
3. Adding two positive binary numbers with overflow.
4. Adding two negative binary numbers without overflow.
5. Adding two negative binary numbers with overflow.

## Slide 18: No Overflow Detection
Full Adder
Full Adder
Full Adder
A0 B0
A1 B1
A2 B2
S0
S1
S2
cin
C2
C1
Full Adder
A3 B3
S3
C3
Full Adder
Full Adder
Full Adder
A4 B4
A5 B5
A6 B6
S4
S5
S6
C6
C5
Full Adder
A7 B7
S7
C7
C4
co
This 8-bit adder does not have overflow detection function. You will have to examine the simulation output to determine if there is overflow.
Show a TA your Tcl script for the FullAdd module tests all possible combinations.
Show a TA your simulation for your Add8 module and explain how you know your circuit is correct and how you know whether overflow occurred.

## Slide 19
10000100 -124
00011001 25
01111100 124
11100111 -25
10000100 (-124) + 01100100 (100) = -24
01111111 (127) + 10011001 (-103) = 24
01111111 (127) + 01100111 (103) = Overflow
00011010 (26) + 01001001 (73) = 99
11100110 (-26) + 10110111 (-73) = -99
10000100 (-124) + 10011001 (-103) = Overflow
10000100 (-124) - 01100100 (100) = Overflow
01111111 (127) - 10011001 (-103) = Overflow
01111111 (127) - 01100111 (103) = 24
00011010 (26) - 01001001 (73) = -47
11100110 (-26) - 10110111 (-73) = 47
10000100 (-124) - 10011001 (-103) = -21

## Slide 20
Add8
8
s[7:0]
8
8
b[7:0]
arithmetic_top
16
sw[15:0]
sw[7:0]
8
led[7:0]
Sub
co
sw[15:8]
a[7:0]
cin
co
Overflow Detector 2
c7
overflow
Overflow Detector 1
overflow
s[7]
✘
a[7]
b[7]
Invert?
✘

## Slide 21: Top-Level Design
Build a top-level module that instances your 8-bit adder module.
Connect sub to cin of the Add8 module.
Include logic gates to negate B if sub is 1.
Include logic gates to detect overflow.

## Slide 22: Detecting Overflow
2’s Complement overflow occurs if:
  Adding two positive numbers gives a negative result
  Adding two negative numbers gives a positive result
2’s Complement overflow can never occur when:
  Adding a positive and a negative number together
  overflow = A[7]B[7]S[7]’ + A [7]’B[7]’S[7];
Detect overflow by looking at the signs

## Slide 23
module arithmetic_top(
input wire logic [15:0] sw,
input wire logic sub,
output logic [7:0] led,
output logic overflow
);
…
overflow = ABS’ + A’B’S;
Add8 OPA(.a(?), .b(?), .cin(?), .s(?), .cout(?));
endmodule
You should use the .port(wire) way of mapping ports on instances to your wires (see Program 11.1.2 in the textbook).

## Slide 24: What is missing?
Use the sub signal to determine if the second operand must be inverted.
Use the sub signal (0 for addition and 1 for subtraction) to complete negating the second operand.
sub | any bit from B | Invert?
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 26: Testbench
TCL is not convenient for testing complex digital circuits.
Testbenches are SystemVerilog files that are used to test your circuit and are not used for designing new logic circuits.
You will be given a SystemVerilog testbench file that will test your circuit for all future labs.

## Slide 27
Adding a Testbench and Simulating with a Testbench
Add the testbench as simulation source.
Select the testbench and Set As Top.
Run Behavioral Simulation.
Enter “run all” in Tcl Console.
Make sure 0 errors.
Check simulation result to debug your circuit.

## Slide 28: Synthesis, Implementation, Bit File
Create and add XDC constraints file
Synthesize
Implement
Download the bit file.