## Slide 1: Lab 5 Seven Segment Decoder
EcEn 220

## Slide 2: Taming Vivado
Under Resources
Multiple copies of Vivado running from other user
Power cycle your entire machine

## Slide 3: Moving Forward
At this point in the semester, we are getting familiar with
  Vivado
  Tcl file
  Testbench
  SystemVerilog Coding Standard
  Structural SystemVerilog
For the rest of the semester, we will focus on circuit design
  Dataflow
  Behavioral
  If your circuit doesn’t work, it is most likely because your design is wrong.
  Do not expect the TAs to help debugging your design.

## Slide 4
a
b
c
d
e
f
g
1
1
1
1
1
1
1
1
1
1
1
1
1
1
a
b
c
d
e
f
g

## Slide 5
a
b
c
d
e
f
g
a
b
c
d
e
f
g
1
1
1
1
1
1
1
0
1
1
1
1
1
1

## Slide 6
a
b
c
d
e
f
g
b
c
d
e
f
g
1
1
1
1
1
1
1
1
0
1
1
1
1
1
a

## Slide 7
a
b
c
d
e
f
g
b
c
d
e
f
g
1
1
1
1
1
1
1
1
1
1
0
1
1
1
a

## Slide 8
a
b
c
d
e
f
g
a
b
c
d
e
f
g
1
1
1
1
1
1
1
1
1
1
1
0
1
1

## Slide 9
a
b
c
d
e
f
g
a
b
c
d
e
f
g
1
1
1
1
1
1
1
1
1
1
1
1
0
1

## Slide 10
a
b
c
d
e
f
g
a
b
c
d
e
f
g
1
1
1
1
1
1
1
1
1
1
1
1
1
0

## Slide 11
a
b
c
d
e
f
g
a
b
c
d
e
f
g
1
1
1
1
1
1
1
1
1
0
1
1
1
1

## Slide 12
a
b
c
d
e
f
g

## Slide 13
a
b
c
d
e
f
g

## Slide 14
a
b
c
d
e
f
g

## Slide 15
a
b
c
d
e
f
g

## Slide 16
a
b
c
d
e
f
g

## Slide 17
a
b
c
d
e
f
g

## Slide 18
a
b
c
d
e
f
g

## Slide 19
a
b
c
d
e
f
g

## Slide 20
a
b
c
d
e
f
g

## Slide 21
a
b
c
d
e
f
g

## Slide 22
a
b
c
d
e
f
g

## Slide 23
a
b
c
d
e
f
g

## Slide 24
a
b
c
d
e
f
g

## Slide 25
a
b
c
d
e
f
g

## Slide 26
a
b
c
d
e
f
g

## Slide 27
a
b
c
d
e
f
g

## Slide 28
a
b
c
d
e
f
g

## Slide 29: Design Process
Block Diagram, specify Inputs/Outputs
Complete a Truth Table
Determine output logic equations
Instance LUT’s
Simulate
Synthesis/Download
Test on the Board

## Slide 30
Seven Segment Decoder
data[0]
data[1]
data[2]
data[3]
CA – segment[0]
Combinational
Logic
CB – segment[1]
CC – segment[2]
CD – segment[3]
CE – segment[4]
CF – segment[5]
CG – segment[6]

## Slide 31
Hex | Input |  |  |  | Output |  |  |  |  |  | 
Character | Binary |  |  |  | Segment [6:0] |  |  |  |  |  | 
0 | data[3] | data[2] | data[1] | data[0] | CG | CF | CE | CD | CC | CB | CA
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1
2 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0
3 | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0
4 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1
5 | 0 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 0
6 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
7 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0
8 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
9 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0
A | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
b | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 1
C | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 0
d | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 1
E | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0
F | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 1 | 1 | 0
a
b
c
d
e
f
g
16’h 1083 16’h 208E 16’h 02BA
16’h 8492
16’h D004
16’h D860
16’h 2812

## Slide 32
Hex | Input |  |  |  | Output |  |  |  |  |  | 
Character | Binary |  |  |  | Segment [6:0] |  |  |  |  |  | 
0 | data[3] | data[2] | data[1] | data[0] | CG | CF | CE | CD | CC | CB | CA
0 | 0 | 0 | 0 | 0 |  |  |  |  |  |  | 
1 | 0 | 0 | 0 | 1 |  |  |  |  |  |  | 
2 | 0 | 0 | 1 | 0 |  |  |  |  |  |  | 
3 | 0 | 0 | 1 | 1 |  |  |  |  |  |  | 
4 | 0 | 1 | 0 | 0 |  |  |  |  |  |  | 
5 | 0 | 1 | 0 | 1 |  |  |  |  |  |  | 
6 | 0 | 1 | 1 | 0 |  |  |  |  |  |  | 
7 | 0 | 1 | 1 | 1 |  |  |  |  |  |  | 
8 | 1 | 0 | 0 | 0 |  |  |  |  |  |  | 
9 | 1 | 0 | 0 | 1 |  |  |  |  |  |  | 
A | 1 | 0 | 1 | 0 |  |  |  |  |  |  | 
b | 1 | 0 | 1 | 1 |  |  |  |  |  |  | 
C | 1 | 1 | 0 | 0 |  |  |  |  |  |  | 
d | 1 | 1 | 0 | 1 |  |  |  |  |  |  | 
E | 1 | 1 | 1 | 0 |  |  |  |  |  |  | 
F | 1 | 1 | 1 | 1 |  |  |  |  |  |  | 
a
b
c
d
e
f
g

## Slide 33: How to choose which digit to display?
There are 4 digits.
A logic value of 0 must be passed to the anode to turn on a digit.
Turn on all 4 digits
  assign anode = 4’b0000;
Turn off all 4 digits
  assign anode = 4’b1111;

## Slide 34: How to turn on the digit point?
Digit point is turned on if the 8th segment (segment[7]) or DP is set to 0.
We will use (press) the center button (btnc) to turn on the digit point.

## Slide 36
Be very careful using internal signals. Make sure the connection is correct.
No signal can be used as output more than once. Signals can be used as input multiple times.
Structural SV (gates like in Lab 3), in non-minimized, sum-of-products form.
Structural SV, minimized using the theorems in Table 4.1 of the textbook.
Dataflow SV, using an assign statement and the ?: (sometimes called the ternary) operator.
Dataflow SV, using an assign statement and dataflow operators of your choice (comparison, and, or, etc.).
module seven_segment_top(
input wire logic [3:0] data,
output logic [6:0] segment,
);
endmodule

## Slide 37: Top-Level
module seven_segment_top(
input wire logic [3:0] sw,
input wire logic btnc,
output logic [7:0] segment,
output logic [3:0] anode
);
endmodule
Be very careful matching the width of signals.
Turn on the digit point when btnc is pressed.
Design this circuit
Turn on the right most digit.
Set the correct anode signal.

## Slide 38
N3 | N2 | N1 | N0 | a
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 1
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 0
Works like a 16 to 1 multiplexer. The “inputs” are constant, according to the INIT string
0010 1000 0001 0010
Rom Logic

## Slide 39
Hierarchy
N0
N1
N2
N3
Combinational
Logic
ROM
Logic
Seven Segment Decoder
CA
CB
CC
CD
CE
CF
CG